## Slide 1: Approach Lighting

## Slide 2: Approach Lighting System (ALS)
The ALS is an airport lighting system that projects light in a directional pattern to help a pilot (i) identify a runway and (ii) align the aircraft with the runway on final approach and landing that:
  Is installed at the approach end of a runway
  Extends outward from the runway
Consists of:
  Series of light bars
  Strobe lights, or a combination of the two.
Usually installed on a runway with an instrument approach procedure

## Slide 3: Approach Lighting System (ALS)
Knowing the type of lights to expect can help you identify the correct runway and avoid landing on the wrong runway at an airport with parallel runways
If you know the type of approach lighting available, other lighting in the airport’s vicinity is less likely to cause confusion

## Slide 4: ALS Components
Threshold Bar - All ALSs begin with a row of green lights that indicate the approach end of the runway
Runway Alignment Indicator Light (RAIL) consists of five sequenced white strobe lights located on the extended runway centerline, the first being located 200 feet beyond the approach end of the last steady-burning light bar (generally 1,000’ from the threshold) with successive strobes at each 200-foot interval out to 2,400 feet from the threshold (may extend to 3,000 feet)
Sequenced Flashing Light (SFL)
  White sequenced strobe lights located on the last three light bar stations
The RAIL and SFL strobes flash in sequence twice per second producing a ball of light streaking toward the approach end of the runway
Click on picture to play the video

## Slide 5: ALS Components
RAIL and SFL provide early identification and alignment / displacement information when approaching a runway
RAIL are not imbedded in the approach lights

## Slide 6: ALS Components Decision Bar
Three light bars (5 steady-burning white lamps on each) that form a crossbar
Serves several functions
  Enables you to determine your physical location from the runway
    On glideslope, when the decision bar passes directly underneath you, you should be approximately 100 feet above the TDZE
    Decision bar is 1,000 feet from the threshold and will generally appear to slip below the airplane's nose at DH
  Serves as an artificial horizon to help transitioning from IMC to VMC at decision height
    Decision bar's horizontal spread of white lights acts like an external attitude indicator, providing you with visual bank references
  Reference point used as a distance-to-go mark

## Slide 7: ALS Components Decision Bar and Light Bars
Allows you to make in-flight visibility estimates
  Distance from the decision bar at DH
  MALSR light bars are spaced at 200 foot intervals
  ALSF 1 / 2 light bars are spaced at 100 foot intervals
Flashing white lights will stop at or before the decision bar (from the approach side)

## Slide 8: Decision Bar Transition to Visual
Decision Bar acts as an
external bank indicator
and assists in the
transition from
Instruments to visual

## Slide 9: ALS May Allow You to Determine Visibility
At a standard decision height of 200’ AGL for an ILS Category I approach you will be approximately 3,846’ from the runway touchdown zone, or 2,846’ from the runway threshold
  on a 3° glide path, if the reported visibility is ½ SM or 2,500’ - you will see very little of the runway environment, if any, other than approach lights

## Slide 10: Visibility Determinations
If an approach procedure requires ½ statute mile flight visibility (+/- 2600'), then if you are able to identify the decision bar at the marker, you would know you have enough flight visibility to continue the procedure
If the middle marker is closer you can use the MALSR and ALSF lights to judge further distances

## Slide 11: ALS Components
Red Terminating and side row bars – Allow descent below 100’ above the touchdown zone - FAR 91.175(c)(3)(i)

## Slide 12: ALS Components
Omnidirectional approach lighting system (ODALS), a flashing light system, similar to a RAIL, but is visible from all directions
  RAIL and sequenced flashing lights are visible only when you are approaching the runway
Runway End Identifier Lights (REIL) - Synchronized flashing high intensity white lights placed in the vicinity of the runway threshold approximately 40 feet from the runway edge and in line with the threshold lights. The lights are directed toward the approach zone, enabling the pilot to identify the runway’s threshold

## Slide 13: Lead-In Lighting System LDIN
LDIN provides positive visual guidance along an approach path, either curving or straight, where special problems exist with hazardous terrain, obstructions, or noise abatement procedures
Consists of one or more series of flashing lights installed along the approach path at or near ground level
The groups of lights are positioned to seen and followed by approaching aircraft
Each light group contains at least three flashing lights in a linear or cluster configuration and may be augmented by steady-burning lights
The lights generally flash in sequence toward the runway
LDIN may be terminated at where the approach lighting system begins

## Slide 14: What dictates the ALS
Types of Approaches to the runway
  ILS or LPV approach with visibility less than ¾-mile, will be an ALSF-2 or 1, a SSALR or MALSR
  CAT II and CAT III runway will have ALSF-2 or 1 lighting

## Slide 15: ALSF
Most complex light structure
Used on runways with CAT II or CAT III approaches
Unique feature of the ALSF-1 and 2 is the red side row or red terminating bars.
  If you can maintain visual contact with the red light bars you can descend below 100’ above TDZE

## Slide 16: ALSF
Most ALSF systems have five intensity levels, or steps
Cat-I approaches only need the first three
  CAT-I lights only reach medium intensity at full brightness, so they are called medium lighting
    truncated e.g. MALSR. The “M” is for medium

## Slide 17: ALSAF-2
ALSF-2 (Approach Lighting System with Sequenced Flashing Lights) is used on Category II runways during instrument landing approach to align the aircraft with the centerline of the runway and to establish vertical orientation
  Steady white lights serve as a reference plane
  Two rows of red side row barrettes increase the pilots horizontal perception
  Sequential white strobe lights that fire in sequence and appear as a ball of light zipping down the ALS centerline, towards the runway, twice a second (aka the “rabbit”)
    Rabbit helps you acquire the ALS and orient you to the runway
This is the system with all the bells and whistles
  2400 feet up to the threshold
    Approaches with slopes of less than 2.75 degrees get an extra six bars to reach 3000 feet
  Gives the pilot a visual indication of crab angle and helps prepare for the landing
But there are versions that are simplified and/or shortened

## Slide 18: ALSF-1
ALSF-1 - less common
Is the same as the ALSF-2 up to the last 1000 feet
ALSF-1 does not have the red side-row bars, but has a wing-shaped pattern of red lights in the last 200 feet to the threshold
  These are the “terminating bars” referenced in FAR §91.175.
    Red side-row lights (ALSF-2) or red terminating bars (ALSF-1)
    Will never have both on the same ALS

## Slide 19: Short Approach Lighting System SALS / SALSF
ALSF-1 is never “simplified”
Can be shortened to 1500’
  Becomes a High Intensity Short Approach Lighting System (SALS) or SALSSF, if sequenced flashing lights are use
Same as inner 1500’ of ALSF-1

## Slide 20: Short Approach Lighting System with RAIL - SSALR
2400’ – 3000’ in length – similar to ALSF-2
An ALSF-2 can, in appropriate weather, be lit as an SSALR
Red side bar turned off
Every other light bar turned off – so 200’ rather than 100’ between bars
Inner bar (500’) side lights turned off
ALSF-2
SSALR

## Slide 21: MALS and SSAL
MALSR (Medium Intensity Approach Lighting System)
SSAL (Simplified Short Approach Lighting System)
Provides visual information to pilots on runway alignment, height perception, roll guidance, and horizontal references generally for category I Precision Approaches

## Slide 22: MALSF and SSALF
Medium Intensity Approach Lighting System with Sequenced Flashers (MALSF)
Same as MALS BUT has three sequenced flashing lights on last 3 light bars
Used where approach area identification is difficult

## Slide 23: MALSR / SSALR
Medium Intensity Approach Lighting System with Runway Alignment Indicator Lights (MALSR)
  Used for CAT I runways
The Simplified Short Approach Lighting System with Runway Alignment Indicator Lights (SSALR) appears identical to the MALSR

## Slide 24: ODALS
Omni-Directional ALS (ODALS)
  Runway end identifier lights (REIL) are part of ODALS
  ODAL adds a 1500-foot RAIL leading to the threshold with no other solid-burning lights

## Slide 25: Approach Plate Presentation
Shown in the information bar
  Symbol
  Graphic depiction
  Textual label

## Slide 27: Disclaimer
Instrument flight can be dangerous. Do not rely solely on this presentation – PROFESSIONAL INSTRUCTION IS REQUIRED
The foregoing material should not be relied upon for flight
ALTHOUGH THE ABOVE INFORMATION IS FROM SOURCES BELIEVED TO BE RELIABLE SUCH INFORMATION HAS NOT BEEN VERIFIED, AND NO EXPRESS REPRESENTATION IS MADE NOR IS ANY TO BE IMPLIED AS TO THE ACCURACY THEREOF, AND IT IS SUBMITTED SUBJECT TO ERRORS, OMISSIONS, CHANGE