## Slide 1
The Missed Approach –
Hey Where’s the Runway?

## Slide 2: Missed Approach Segment
A Missed approach is a procedure used when an instrument approach cannot be completed to a full-stop landing
The Missed Approach Segment is that part of an instrument approach procedure between the missed approach point (MAP), the missed approach way-point (MAWP), or the point of arrival at the decision height and the specified missed approach NAVAID (navigational aid), intersection, fix, or waypoint, as appropriate, at the minimum IFR altitude
  It is in this part of the approach procedure that the aircraft will climb and return to the en route structure or is positioned for holding or subsequent approach
  The missed approach route and altitudes are shown on the instrument approach charts

## Slide 3: The Missed Approach
The missed approach is one of the most difficult and critical phases of an instrument approach and is the one practiced the least
  High workload, as the configuration of the aircraft must be changed (approach to climb out), coupled with new navigation route/Navaids
  An approach in actual conditions should be flown with the anticipation that the missed approach is an anticipated outcome
The missed approach procedure typically includes an initial heading or track to follow, and an altitude to climb to. This is typically followed by holding instructions at a nearby navigation fix
Be sure you have reviewed the missed approach procedure BEFORE the FAF

## Slide 4: Missed Approach Anatomy
Start of climb
Obstacle clearance rate of 1 foot vertically for each 40 feet horizontally

## Slide 5: How Did We Get to a Missed Approach FAR 91.175(e)
A missed approach procedure must be immediately executed:
  1. Whenever:
    Flight visibility is less than the specified visibility for the approach
    If required visual references are not seen at either of the following times:
      When the aircraft is being operated below MDA; or
      Upon arrival at the missed approach point, including a DA/DH where a DA/DH is specified and its use is required, and at any time after that until touchdown.
  2. Whenever an identifiable part of the airport is not distinctly visible to the pilot during a circling maneuver at or above MDA, unless the inability to see an identifiable part of the airport results only from a normal bank of the aircraft during the circling approach

## Slide 6: Visual References FAR 91.175(c)(3)
Except for certain Category II or III approaches, at least one of the following visual references for the intended runway must be distinctly visible and identifiable to the pilot to continue below the DH or MDA:
  The approach light system, except you may not descend below 100 feet above the touchdown zone elevation using the approach lights as a reference unless the red terminating bars or the red side row bars are also distinctly visible and identifiable
  The threshold
  The threshold markings
  The visual approach slope indicator
  The threshold lights
  The runway end identifier lights (REIL)
  The touchdown zone or touchdown zone markings
  The touchdown zone lights
  The runway or runway markings
  The runway lights
Basic rule of thumb you need to distinctly see the runway and/or its lighting

## Slide 7: Also Go Missed If:
A safe approach or landing is not possible
Full scale needle deflection past the final approach fix
Navigation equipment required for the approach fails
ATC instructs you to go missed
  Unsafe runway
  Traffic
  Controller or pilot navigation errors
Weather – e.g., thunderstorm cell
When the aircraft is being operated below MDA – loss of visual references
If your gut says something is wrong or unclear

## Slide 8: Missed Approach Clearance
A clearance for an instrument approach procedure includes a clearance to fly the published missed approach procedure, absent contrary ATC instructions

## Slide 9: Missed Approach Procedures
Published Missed Approach Instructions
  If ATC has not issued specific instructions prior to the approach and a missed approach is executed, the pilot must follow the published or default missed approach procedure
  A controller may issue modified instructions, which supersede the published instructions
Verbal Missed Approach Instructions
  ATC may give you instructions for the missed approach prior to the clearance for the approach
    ATC will give you altitude, heading, frequency, and supplementary information as required
      ATC: "Missed approach instructions, climb [Altitude], turn left [Heading] and contact departure [Frequency]. Be advised [Traffic...]“
If executing instructions different from those on the procedure as dictated by approach, call “on the go" or "executing climb out" to reduce confusion

## Slide 10: Missed Approach Chart Symbols
To provide ready missed approach guidance, approach plates use quick reference icons
  Due to limited space only four or less icons can be shown. Hence the icons may not show the entire missed approach procedure
  The full missed approach instructions are provided textually at the top of the approach chart in the pilot briefing

## Slide 11: JEPP Missed Approach Chart Symbols

## Slide 12: NACO Missed Approach Chart Symbols
Climb to altitude
Turn to specified heading
To Specified fix
Track Radial

## Slide 13: Missed Approach Point Location
The missed approach point (MAP) on a non-precision approach is not designed with any consideration to where the aircraft must begin descent to execute a safe landing
  It is developed based on terrain, obstructions, NAVAID location and possibly air traffic considerations
  Descent below the MDA, including during the missed approach, is not authorized
The Decision Altitude (DA) is an altitude derived location where a missed approach will be initiated on a precision approach
  Obstacle clearance is provided to allow a momentary descent below DA while transitioning from the final approach to the missed approach
  Decision Altitude (DA) replaces the familiar term Decision Height (DH).

## Slide 14: Obstacle Protection
Obstacle protection is predicated on the missed approach being initiated at the DA/H or at the missed approach point and not lower than minimum descent altitude (MDA)
A climb gradient of at least 200 feet per nautical mile is required, unless a higher climb gradient is published in the notes section of the approach procedure chart
  When higher than standard climb gradients are specified, the end point of the non-standard climb will be specified at either an altitude or a fix
Preplan your approach to ensure you can meet the climb gradient (expressed in feet per nautical mile)
  Higher than anticipated ground speed increases the climb rate requirement (feet per minute)
  Tables for climb gradients (feet per nautical mile) to climb rate (feet per minute), based on ground speed, are on page D1 of U.S. Terminal Procedures booklets
  Formula: Required Climb Per Minute = ((_[climb gradient]_ ft/nautical mile) x ([ground speed] nautical miles/hour)/60) = 36,000 feet per hour =

## Slide 15: Beginning the Procedure Other Than at the MAP/DH
In the design of the missed approach procedure no consideration is given to an abnormally early missed approach turn from the approach course
When an early missed approach is executed, pilots should, unless otherwise cleared by ATC,
  Fly the IAP as specified on the approach plate to the missed approach point
  Remain at or above the MDA or DH before executing a turning maneuver
  Can begin climb early, absent altitude restrictions
Think CFIT when making an early missed!!

## Slide 16: Circling Approach MAP
Executing the missed approach after starting the circling maneuver usually places the aircraft beyond the MAP
The missed approach is executed for the runway the approach started on, not the runway you were circling to
The initial turn on a missed approach will always be towards the landing runway until established on a segment of the missed approach
Always think about how to execute the missed approach while circling so it is not a surprise if you enter IMC as aircraft is clear of obstacles only when at or above the MDA while inside the circling area
Since the circling missed approach maneuver may be accomplished in more than one direction, different patterns will be required to become established on the prescribed missed approach course, depending on the aircraft position at the time visual reference is lost.

## Slide 17: Flying the Missed Approach
Before the FAF
  Memorize initial altitudes and headings
  Set up No. 2 Nav if possible for missed approach initial navaid course

## Slide 18: Flying the Missed Approach Initial Missed Approach Segment Procedure
At the MAP / DA
  Add climb power
  Rotate gradually (on-speed) to Vx
  Check for positive rate of climb
  Clean up the aircraft – gear and flaps up in the order specified by the POH
  Climb out at appropriate speed

## Slide 19: Communicate
Upon execution of a missed approach and becoming stabilized in climb notify ATC
  If communicating with the Tower - "[Place] tower, [Callsign], missed approach [Reason]"
  If communicating with approach - "[Place] approach, [Callsign] missed approach off of [Location] climbing through [Altitude] for [Altitude] with request"

## Slide 20: Lost Communications Missed Approach
If communications are lost during the approach and you take a missed approach:
  Squawk 7600
  Follow the published missed approach instructions to ensure adequate obstruction clearance
  Route:
    Proceed to the alternate IAF as filed and commence an approach
  Altitude:
    The EXPECTED altitude, if given one, after filing a “DRAFT” or;
    Your option of the highest of the two emergency safe altitudes depicted on the destination and alternate approach procedure charts if fields are within 200 NM of each other or
    At flight level 18,000'
      If destination altimeter is 29.92 inches or higher, fly FL180
      If destination altimeter is less than 29.92, fly FL190
"DRAFT": Short flight plan including - a) Destination; b) Route; c) Altitude; d) Fuel State and e) Time En-route

## Slide 21: NOW WHAT
Decide what your course of action will be
  Repeat the same approach at the same airport
  Another approach at the same airport
  Divert to planned alternate
  Divert elsewhere
  Hold for conditions to improve
Consider fuel load and distance / time to a good alternate
Inform ATC of your desires

## Slide 22: Alternate Missed Approach
Some locations may have a preplanned alternate missed approach procedure for use in the event the primary NAVAID used for the missed approach procedure is out of service
To avoid confusion, the alternate missed approach instructions are not published on the chart
  However, the alternate missed approach holding pattern will be depicted on the instrument approach chart
When the alternate missed approach procedure is implemented by NOTAM, it becomes a mandatory part of the procedure. The NOTAM will specify both the textual instructions and any additional equipment requirements necessary to complete the procedure
You may reject an ATC clearance for an alternate missed approach that requires equipment not necessary for the published approach procedure when the alternate missed approach is issued after beginning the approach
  However, if the alternate missed approach is issued prior to beginning the approach the pilot must either accept the entire procedure (including the alternate missed approach) or request a different approach procedure

## Slide 23: G1000 Missed Approach
At the MAP, “SUSP” is displayed in the HSI and directly above the SUSP softkey
  Automatic sequencing of approach waypoints is suspended at the MAP
  A “FROM” indication is displayed on the CDI, but the course guidance is simply an extension of the final approach course
    Do NOT follow this extended course
When the message “RAIM is not available” is displayed in the Alerts Window on the PFD a missed approach must also be executed

## Slide 24: G1000 Missed Approach
Flying the Missed
  Initiate the missed approach sequence by following the missed approach procedures as published / directed by ATC, for proper climb and heading instructions
  If not already using GPS as nav source, press the CDI softkey to switch external CDI output to GPS for guidance.
  Press the SUSP softkey to return to automatic sequencing of waypoints
  If there is a missed approach course from a fix to altitude, Within a few seconds of pressing the SUSP softkey , “SUSP” is re-displayed above the SUSP softkey
    Upon reaching the desired altitude, press the SUSP softkey to resume automatic leg sequencing
    After pushing SUSP, “NEXT DTK 123” message is displayed in the navigation status bar on the PFD
  The G1000 will guide to the missed approach holding point and a recommended entry procedures for the holding pattern will be shown

## Slide 25: G1000 Missed Approach
Note that the G1000 at the holding point again displays “SUSP” above the SUSP softkey. Automatic waypoint sequencing is suspended at the missed approach holding point. The waypoint message (ARRIVING AT WAYPOINT) is displayed each time the plane approaches the holding fix in the holding pattern
The G1000 provides course guidance only on the inbound side of the holding pattern
  When leaving the holding pattern to re-fly the approach, press the PROC key to “Select Approach” or “Activate Approach” (or use the Direct-To key to select another destination)

## Slide 26: G1000 Missed Approach Example Missed Approach Course From Fix To Altitude
  After pressing the SUSP softkey, the missed approach sequence is automatically started with the course from fix to altitude leg
  After pushing SUSP, “NEXT DTK 123” message is displayed in the navigation status bar on the PFD
  Within a few seconds of pressing the SUSP softkey , “SUSP” is re-displayed above the SUSP softkey - The G1000 returns to suspend mode when flying a course from a fix to altitude leg and indicates that automatic leg sequencing is suspended
  Fly the outbound course keeping the CDI needle centered. The Navigation Map Page depicts the flight path extending indefinitely from the Navfix. The distance increases and indicates the distance back to the Navaid
  Upon reaching the desired altitude, press the SUSP softkey to return to automatic leg sequencing. Confirm that ‘SUSP’ no longer is displayed directly above the SUSP softkey
  The message “NEXT DTK 123” is the displayed, providing guidance to the holding fix. The actual desired track (DTK) depends on the ground speed and distance from the Navaid. Intercept and fly the inbound course, keeping the CDI needle centered
  As the plane approaches the Navaid (the missed approach holding point), a message in the navigation status bar recommends the holding pattern entry, e.g., “HOLD PARALLEL”
  Note that the G1000 again displays ‘SUSP’ above the SUSP softkey. Automatic waypoint sequencing is suspended at the missed approach holding point. The waypoint message (ARRIVING AT WAYPOINT) is displayed each time the plane approaches the holding fix in the holding pattern
  When leaving the holding pattern, press the PROC key to reactivate the approach or select a different approach, or press the Direct-To key to select another destination

## Slide 27: G1000 Missed Approach Additional Automation
GA Switch (Go-Around)
  Disengages the autopilot
  Selects the flight director Go-Around Mode, and
  Activates the missed approach
  The GA Switch is located on the instrument panel above the throttle
TOGA (Takeoff/Go-Around) Switch
  Offers automated go-arounds
  At the MAP, press the TOGA button
    Keeps the AP engaged
    Commands a climb
    Sets Autopilot to NAV mode and
    Sequences to the missed approach

## Slide 28: Pitch-up Illusion
Pitch-up illusion is a significant hazard during the transition to climb out
On approach the portion of the inner ear that provides sensory information related to acceleration—provides the sensation of stabilized speed, based primarily on the forces of gravity
When acceleration and climb occur simultaneously as during the initial segment of a missed approach, two forces come together - gravity and acceleration
The brain resolves the two forces (gravity and acceleration) as a single resultant force acting downward and backward. The brain incorrectly resolves the two forces as a single pitch-up movement
When that occurs, the pilot feels as though the aircraft is climbing or that the nose is pitching up, when, in fact, it remains in level flight.
The normal reaction, absent visual clues, to the pitch-up illusion is to push forward on the stick with the risk of ground contact in a missed approach

## Slide 29: Common Errors
Failure to have essential knowledge of the information on the approach chart
Failure to have initial steps of missed approach committed to memory
Failure to identify DH or MAP or other condition requiring a missed approach
Incorrect communication procedures
Noncompliance with ATC clearances, the published missed approach or an ATC instruction or failure to notify ATC of inability to comply
Failure to accomplish checklist items
Faulty basic instrument flying techniques
Failure to accomplished a missed approach timely – e.g. motoring on to look for references

## Slide 30: PTS Standards Area of Operation VI. C.
Executes the missed approach procedure when the required visual references for the intended runway are not distinctly visible and identifiable:
  Non-Precision Approach – at the MAP
  Precision Approach - at Decision Altitude

## Slide 31: PTS Standards Area of Operation VI. C.
Adequate knowledge of the missed approach procedure elements for standard approaches
Initiates the missed approach promptly by applying power, establishing a climb attitude, and reducing drag in accordance with the aircraft manufacturer’s recommendations
Reports beginning the missed approach procedure to ATC
Complies with the published or alternate missed approach procedure
Advises ATC or examiner anytime that the aircraft is unable to comply with a clearance, restriction, or climb gradient
Follows the recommended checklist items appropriate to the go-around procedure
Requests, if appropriate, ATC clearance to the alternate airport, clearance limit, or as directed by the examiner
Maintains the recommended airspeed within ±10 knots; heading, course, or bearing within ±10°; and altitude(s) within ±100 feet during the missed approach procedure.
Uses MFD and other graphical navigation displays, if installed, to monitor position and track to help navigate the missed approach.
Demonstrates an appropriate level of single-pilot resource management skills.

## Slide 32: Questions

## Slide 33: Disclaimer
Instrument flight can be dangerous. Do not rely solely on this presentation – PROFESSIONAL INSTRUCTION IS REQUIRED
The foregoing material should not be relied upon for flight.
ALTHOUGH THE ABOVE INFORMATION IS FROM SOURCES BELIEVED TO BE RELIABLE SUCH INFORMATION HAS NOT BEEN VERIFIED, AND NO EXPRESS REPRESENTATION IS MADE NOR IS ANY TO BE IMPLIED AS TO THE ACCURACY THEREOF, AND IT IS SUBMITTED SUBJECT TO ERRORS, OMISSIONS, CHANGE.