## Slide 2: General Rules
When completing a flight plan the following rules apply:
  Use capital letters, one letter in each space of the field (unless field are not divided into spaces)
  Adhere to the prescribed formats and manner of specifying data
  Data should only be inserted only in the fields and spaces provided
  Where excess space is available, leave unused spaces blank
  All times should be clock times in 4 figures UTC (e.g., 1800, 0930, etc.)
  Special characters may not be used in ICAO remarks: the forward slash “/”, the dash “-“, and the left and right parentheses “(” and “)”
The item numbers on the form are not consecutive (they correspond to item order in standard ATS messages)
Items preceding item 7 are to be completed by ATC and COM services
Items 7 to 18 should be completed by you
Item 19 completion is to facilitate alerting of Search and Rescue

## Slide 3: FAA Quick Guide
Recommend keeping a copy of the FAA flight plan guide available at https://www.faa.gov/about/office_org/headquarters_offices/ato/service_units/air_traffic_services/flight_plan_filing/media/FPL_Brochure_(change3).pdf

## Slide 4
These items (Items preceding item 7) will be completed by ATC

## Slide 5
Aircraft Identification –
  Insert N Number
  Insert CAP A/C ID – e.g. CAP4272
  No hyphens or spaces
Flight Rules
  I for IFR
  V for VFR
  Y for IFR first, then VFR
  Z for VFR first, then IFR
Type of Flight
  G - General Aviation
  M - Military
  D – DVFR
  X - Other than any of the defined categories above

## Slide 6
Number
  Number of aircraft in flight, if more than one.
  Omitted if only a solo aircraft movement.
Type of Aircraft
  C172, C182, GA8
  Designators available at http://www.icao.int/publications/DOC8643/Pages/Search.aspx
Wake Turbulence Cat
  “L” for Light (< 15,500 lbs)

## Slide 7
Equipment
  Must show Equipment and capabilities for:
    Navigation
    Transponder
    ADS-B

## Slide 8
Navigation (before the slash)
  To simplify filing, the code “S” can be included to indicate Standard Capabilities - VHF RTF/VOR/ILS. Removes the need to list these three capabilities separately.
  Other Codes
    B - LPV (APV/SBAS) - Localizer Performance with Vertical Guidance (Satellite based augmentation)
    D - DME - Distance Measurement Equipment
    F - ADF - Automatic Direction Finder
    G - GNSS – GPS (When using the letter “G” on an IFR flight plan,
    the GPS receiver must be IFR approved)
    ATC RTF SATCOM (Multiple) – Satellite phone
    L - ILS - Instrument Landing System
    O - VOR - VHF Omnidirectional Radio Range
    R - PBN - Performance-Based Navigation
    V - VHF RTF - VHF Radiotelephone
    Y - VHF 8.33 - 8.33 kHz Radio Channel Spacing (Where you can select the 3rd decimal place when tuning in a frequency (e.g. 122.975 vs. 122.97))
    Z - OTHER - Other Item(s) Not Listed Above – specify in item 18
    N - No navigation, communications, or approach capability

## Slide 9: Performance Based Navigation
For Garmin GPS’, Garmin has published a capability listing - https://fly.garmin.com/fly-garmin/support/icao-flight-plans#modal-eula

## Slide 10
Transponder (Remember to add the “/” between COM/NAV equipment codes and transponder code)
  A- No mode C
  C – Mode C
  Mode S
ADS-B=Extended squitter
For example - Aircraft with VHF, VOR, ADF, ILS, DME, HF, Mode A and Mode C transponder – insert SDH/C

## Slide 11
ADS B (After the slash)
  ADS B IN – No coding
UAT = Universal Access Transceiver

## Slide 12
Departure Aerodome
  Put in departure airport code – e.g. KSGR
  If the airport identifier is not a four character ICAO identifier, then put “ZZZZ” in the departure airport field. The non ICAO identifier must be specified in Field 18
Time
  Planned time of departure (UTC) in 24-hour “HHMM” format

## Slide 13
Cruising speed in Knots
  “N” for Knots, followed by a four-digit figure – N0110
  Speed used is for the first or the whole cruising portion of the flight
Level – Flight Level (for the first leg or the whole route)
  F - for Flight Level in 100s of feet (three digit)
  A - for plain altitude in 100s of feet (three-digit)
    A065 = 6,500 feet msl
  V - uncontrolled VFR (number field left blank)
Route
  No change from current
  If the departure airport is not on, or is not connected to the ATS route, insert the letters DCT, followed by the joining point of the first ATS route and followed by the designator of the ATS route – e.g. DCT ELA V198 …
  Then insert each point at which either a change of speed or level, a change of ATS route, and/or a change of flight rules is planned
  Example: ELA/N0120A080 IFR (which means that at ELA VOR you are to change speed to 200 knots, altitude to 8000 feet and request to change flight rules to IFR).

## Slide 14
Destination Aerodome
  Put in destination airport code – e.g. KSGR
  If the airport identifier is not a four character ICAO identifier, then put “ZZZZ” in the destination airport field. The non ICAO identifier must be specified in Field 18
Total EET
  Estimated time enroute HHMM - NOT the planned time of landing
Alternate Aerodrome
  Put in alternate airport code – e.g. KSGR
Alternate Aerodrome
  Put in second alternate airport code

## Slide 15
The sequence that indicators should appear in is compulsory
Any given indicator can only appear ONCE in Field 18
Hyphen (-) and slash (/) characters forbidden in data
STS/ indicator is not a free-text field
  Search and Rescue = STS/SAR
PBN/ is now mandatory to detail Performance based navigation equipment capabilities
NAV/ entry is required when GPS equipment is specified

## Slide 16
Indicator Codes
  STS/ - Indicators for Special Handling by ATS
  PBN/ - RNAV and/or RNP Capability Indicators
  NAV/ - Nav. equipment data and GNSS Augmentation
  COM/ - Comm. Equipment Not Specified in Field 10
  REG/ - Aircraft Registration if Different Than Field 7
    e.g. REG/N1472F whereas field 10 is CAP4212
  EET/ - Estimated Enroute Time(s) in “HHMM” format to Significant Fixes or FIR Boundaries
  RMK/ - Plain Language Remarks Where Necessary

## Slide 17
Indicator Codes Con’t
  ALTRV/ – for flight with specified altitude reservation
  PER/ followed by performance of the aircraft according to ICAO document 8168 (categories “A”,”B”,”C”,”D”,”E”
  ORGN/ followed by contact details to flight plan originator.

## Slide 18
DEP/” followed by the name of the departure airport or bearing and distance to navaid/navigation point closest to departure point (if no designator is assigned and “ZZZZ” is inserted in item 13).
“DEST/” followed by the name of the destination airport or bearing and distance to navaid/navigation point closest to destination point (if no designator is assigned and “ZZZZ” is inserted in item 16).
“DLE/” followed by details related to delay enroute (for example for the need of flight training). A place in space should be described as in, for example, DEP/ item, either by navaid or bearing and distance from a significant point enroute, along with duration of the delay.
  DLE/ELA0030 – delay over ELA VOR for 30 minutes
  DLE/HULLO2300200040 – delay at point 230 degrees and 20 NM from HULLO intersection, duration 40 minutes

## Slide 19
If your flight plan is for a future date, make sure that the date is provided clearly in item 18 (preceded by “DOF/”)
You may file a flight plan up to 120 hours before your estimated departure time
The date of the flight in a six-figure format- YYMMDD
  DOF/170613 (which indicated that the flight will take place on 13th of June 2017)

## Slide 21
Endurance
  Total fuel endurance in “HHMM” format
Persons on Board
  Total number of persons (passengers and crew)
  “TBN” (To Be Notied) if number is unknown at filing time
Emergency Radio
  Select “UHF” or “U” here if you are able to receive and xmit at 243.0MHz,
  “VHF” or “V” if you are able to receive and xmit at 121.5 MHz
  “ELT” if an emergency locator beacon is onboard

## Slide 22
Survival Equipment
  Check if equipment is present
Jackets
  Click if life jackets are on-board
    Select “LIGHT” if life jacket(s) have lights
    Select “FLUORES” if jackets have fluorescein strips
    Select “UHF” or “VHF” if jackets are radio equipped

## Slide 23
Dinghies (liferafts)
  Number
    Blank if none otherwise enter number of rafts
  Capacity
    Total aggregate capacity, in persons, of all life rafts carried
    Blank if none
  Cover
    Check this box if the life rafts have protective canopies
  Color
    Plain text description of the life raft’s primary color.

## Slide 24
Plain text description of aircraft color and any significant livery markings or characteristics
  “Red white blue CAP logos”

## Slide 25
Indicate any other survival equipment carried and/or other remarks specifically regarding survival equipment and search-and-rescue (SAR) information

## Slide 26
Name and preferably phone contact information of the pilot in command
  Doe 713-555-1212

## Slide 27
To be completed by ATC

## Slide 28: Questions
For more information see - https://www.capmembers.com/media/cms/N7110_95688ABC3F815.pdf - Air Traffic Organization Policy - N JO 7110.601