ELT Checklist (Becker SAR-DF 517)

Power Up DCU (Display Control Unit)

Aircraft Master Power – On On/Off button – Press Page Mode (upper right corner of DCU) – Emergency or Training – Depending on mission missions * Note: Page select will only appear during first 5 seconds when unit is powered up. Turn off and re-power up if you cannot get the right freq. Freq Select (lower right corner of DCU) – 121.5/406 – 121.775 Dim – Press Rep and turn Page dial simultaneously to desired brightness Page – Turn to desired page (displayed upper right corner of LED display) Volume – Adjust to desired level (lower left corner of DCU) Squelch – Adjust so that it is above noise level

Bearing

Observer – Adjust page dial to 360 deg mode Observer – Direct course changes to pilot based off of bearing received from DCU (* Note number on DCU is a relative bearing from the nose of the aircraft NOT aircraft heading indicator) Observer – Adjust page dial to 90 deg mode Observer – Direct course changes to pilot based off of bearing received from DCU Observer – Adjust receiving level to a lower signal strength, no higher than 50% Crew – Transition into visual search