## Slide 1: IFR Lost Communications I Can’t Hear You Procedures

## Slide 2: Lost Communications
Preflight plan for lost communications
  Where are the cloud tops and which way to nearest VFR
  What is destination weather and alternate
Trouble shoot com problem BUT don’t forget to fly the plane
  Stuck microphone
  Unplug mic and adjust squelch
  Check audio selector
  Confirm frequency
  Try another radio
  Check power / circuit breaker / avionics switch
  Reduce electrical load, if appropriate
  Squawk 7600

## Slide 3: Flying the Lost Comm Plan FAR §91.185
VMC - If the failure occurs in VFR conditions, or if VFR conditions are encountered after the failure, you must continue the flight under VFR and land as soon as practicable and notify ATC
  Not intended that the requirement to "land as soon as practicable" be construed to mean "as soon as possible“
  Primary objective is to preclude extended NORDO IFR operations in VMC

## Slide 4: Flying the Lost Comm Plan - Route FAR §91.185
IMC – Continue in accordance with the following:
  Route – in this order
    By the route assigned in the last ATC clearance received
    If being radar vectored, by the direct route from the point of radio failure to the fix, route, or airway specified in the vector clearance
    In the absence of an assigned route, by the route that ATC has advised may be expected in a further clearance; or
    In the absence of an assigned route or a route that ATC has advised may be expected in a further clearance, by the route filed in the flight plan
as Assigned
as Vectored
as Expected
as Filed.

## Slide 5: Flying the Lost Comm Plan - Altitude FAR §91.185
IMC – Continue in accordance with the following:
  Altitude - At the highest of the following altitudes or flight levels for the route segment being flown:
    The altitude or fight level assigned in the last ATC clearance received;
    The minimum altitude for IFR operations; or
    The altitude or flight level ATC has advised may be expected in a further clearance

## Slide 6: Flying the Lost Comm Plan – Altitude Up and Down
2000
4000
Cessna 1472F cleared to Sugar Land airport, climb and maintain 2000, expect 3,000 ten minutes after departure, departure frequency is …..
Comms lost
10 mins
Fly 2,000 – as assigned and MEA
Climb to 3,000 after 10 minutes
Climb to 4,000 for higher MEA
Descend to 3,000 – for expected altitude
Climb to 5,000 for higher MEA
2000
5000

## Slide 7: Flying the Lost Comm Plan Off-Route Altitudes
If off-route - Maintain the last assigned altitude or the minimum safe/sector altitude (emergency safe altitude if more than 25 NM from the facility), whichever is higher, until established on a segment of the published approach

## Slide 8: Flying the Lost Comm Plan Leaving a Clearance Limit
When the clearance limit is a fix from which an approach begins, commence descent or descent and approach as close as possible to the expect-further-clearance time if one has been received, or if one has not been received, as close as possible to the estimated time of arrival as calculated from the filed or amended (with ATC) estimated time en route.
If the clearance limit is not a fix from which an approach begins, leave the clearance limit at the expect-further-clearance time if one has been received, or if none has been received, upon arrival over the clearance limit, and proceed to a fix from which an approach begins
Commence descent or descent and approach as close as possible to the estimated time of arrival as calculated from the filed or amended (with ATC) estimated time en route.

## Slide 9: Lost Communications
Lost communications is an emergency under IFR conditions. You can deviate as necessary to resolve the problem
During radio failure, when confronted with a situation not covered in the regulation, pilots are expected to exercise good judgment in their actions
Set transponder to 7600
Expect ATC to attempt to communicate with you by transmitting on guard frequencies and available frequencies of navaids
ATC may ask you to acknowledge communications by pressing ident on transponder

## Slide 11: Disclaimer
Instrument flight can be dangerous. Do not rely solely on this presentation – PROFESSIONAL INSTRUCTION IS REQUIRED
The foregoing material should not be relied upon for flight
ALTHOUGH THE ABOVE INFORMATION IS FROM SOURCES BELIEVED TO BE RELIABLE SUCH INFORMATION HAS NOT BEEN VERIFIED, AND NO EXPRESS REPRESENTATION IS MADE NOR IS ANY TO BE IMPLIED AS TO THE ACCURACY THEREOF, AND IT IS SUBMITTED SUBJECT TO ERRORS, OMISSIONS, CHANGE