###### EMERGENCY PROCEDURES

1985 Cessna 172P – N98463

Air Plains 180 HP Conversion

Serial No. 1727401 and subsequent

Engine Failure During Takeoff Roll

- Throttle	Idle

- Brakes	Apply

- Flaps	Retract

- Mixture	Idle Cut Off

- Ignition Switch	Off

Engine Failure Immediately After Takeoff

- Airspeed

70 KIAS (Flaps Up)

65 KIAS (Flaps Down)

- Mixture	Idle Cut Off

- Fuel Selector	Off

- Ignition	Off

- Wing Flaps	As Required

- Master Switch	Off

Engine Failure During Flight (Restart)

- Airspeed	75 KIAS

- Carb Heat	On

- Fuel Selector	Both

- Mixture	Rich

- Ignition	Both

(or START if propeller is

stopped)

- Primer	In & Locked

Forced Landing Without Engine Power

- Airspeed	70 KIAS (Flaps Up)

65 KIAS (Flaps Down)

- Mixture	Idle Cut Off

- Fuel Selector	Off

- Ignition	Off

- Wing Flaps	As Required (30º

Recommended)

- Master Switch	Off

- Doors	Unlatched

Prior To Touchdown

- Touchdown	Slightly Tail Low

- Brakes	Apply Heavily

Precautionary Landing With Engine Power

- Wing Flaps	20°

- Airspeed	65 KIAS

- Select Field	Perform

Fly Over Inspection

- Radio & Electrical Switches 	Off

- Flaps	30º on Final Approach

- Airspeed	65 KIAS

- Avionics & Master Switches	 Off

- Doors	Unlatched

Prior To Touchdown

- Touchdown	Slightly Tail Low

- Ignition Switch	Off

- Brakes	Apply Heavily

Engine Fire During Start

- Continue Cranking Engine

- If Engine Starts:	Power

1700 RPM for a few minutes

- Engine	Shutdown and Inspect

If Engine Fails to Start:

- Throttle	 Full Open

- Mixture	Idle Cut Off

- Cranking	Continue

- Fire Extinguisher 	Obtain

- Master/Ignition/Fuel	Off

- Fire	Extinguish

- Fire Damage	Inspect

Engine Fire in Flight

- Mixture	Idle Cut Off

- Fuel Selector	Off

- Master Switch	Off

- Cabin Heat & Air	Off

(Except Overhead Vents)

- Airspeed	100 KIAS

(If fire is not extinguished, increase glide speed to find an airspeed, which will provide an incombustible mixture.)

- Forced Landing w/o Engine Power	Execute

Electrical Fire in Flight

- Master Switch	Off (Leave Ignition On)

- All Other Switches (Except Ignition)	Off

- Vents/Cabin Air/Heat	Closed

- Fire Extinguisher	Activate

If fire is extinguished & electrical power is necessary

- Master Switch	On

- Circuit Breakers	Check for

Faulty circuit (Do Not Reset)

- Radio/Electrical Switches on one at a time w/ delay after each to locate short.

- Vent cabin when assured fire is extinguished

Cabin Fire

- Master Switch	Off (Leave Ignition On)

- Vents/Cabin Air/Heat	Closed

- Fire Extinguisher	Activate

4. Land	As soon as possible and

inspect damage

Wing Fire

- Navigation Lights	Off

- Strobe Lights	Off

- Pitot Heat	Off

- Landing/Taxi Lights	Off

Note

Sideslip to keep flames away from the fuel tank and cabin, and land as soon as possible using flaps only as required for final approach and touchdown.

Icing

- Pitot Heat	On

- Turn back or change altitude to obtain an outside air temp that is less conducive to icing.

- Pull cabin heat control to full out and open defroster outlet to obtain maximum windshield defroster airflow.

- Open the throttle to increase engine speed and minimize ice build-up on propeller blades

- Watch for signs of carburetor air filter ice and apply carburetor heat as required. An unexplained loss in engine speed could be caused by carburetor ice or air intake filter ice. Lean the mixture if carb heat is used continuously.

- Plan a landing at the nearest airport.  With an extremely rapid ice build-up, select a suitable “off airport” landing site.

- With ice accumulation of ¼ inch or more on the wing leading edges, be prepared for significantly higher stall speed.

- Leave wing flaps retracted. With a severe ice build-up on the horizontal tail, the change in wing wake airflow direction caused by wing flap extension could result in a loss of elevator effectiveness.

- Open left window and if practical scrape ice from a portion of the windshield for visibility in landing approach.

- Perform landing approach using a forward slip, if necessary, for improved visibility.

- Approach at 80 to 90 KIAS depending upon the amount of accumulation.

- Perform a landing in level attitude.

Ditching

- Radio	Transmit Mayday on

121.5 giving location and intentions and squawk 7700.

- Heavy Objects	Secure or

Jettison.

- Flaps	20º to 30º

- Power	Est. a 300 FPM

descent at 55 KIAS.

- Approach

High winds, heavy seas	Into

the Wind.

Light winds, heavy swells

Parallel to swells.

Note

If no power is available, approach at 70 KIAS with flaps up or at 65 KIAS with 10º flaps.

- Cabin Doors	Unlatch

- Touchdown	Level attitude

at established descent rate.

- Face	Cushion at touchdown

with folded coat or seat cushion.

- Airplane	Evacuate through

Cabin doors. If necessary, open window and flood cabin to equalize pressure so doors can be opened.

- Life vests and raft	Inflate

### For all other

Emergency

Abnormal

Procedures.

See the

POH

Section 3.

Airspeeds for Emergency Operations

Engine Failure After Takeoff:

Wing Flaps Up -- 70 KIAS

Wing Flaps Down -- 65 KIAS

Maneuvering Speed:

2550 Lbs – 105 KIAS

2150 Lbs – 95 KIAS

1750 Lbs – 85 KIAS

Maximum Glide:

2550 Lbs – 68 KIAS

2150 Lbs – 62 KIAS

1750 Lbs – 56 KIAS

Precautionary Landing With

Engine Power – 65 KIAS

Landing Without Engine Power:

Wing Flaps Up – 70 KIAS

Wing Flaps Down – 65 KIAS

This checklist is a guide to coordinate Pilot Operating Handbook and STC data applicable to this particular aircraft only.  The applicable Pilot Operating Handbook and STC installations remain the official documentation for this aircraft.

The pilot in command is responsible for complying with all items in the Pilot Operating Handbook and applicable STCs.

I certify this checklist has been reviewed for accuracy.

____________________________________

Wing Director of Maintenance           Date

# Text boxes

Warning

After discharging an extinguisher within a closed cabin, ventilate the cabin.

Warning

After discharging an extinguisher within a closed cabin, ventilate the cabin.